The relevance of Superlattice Multiplier Technologies for Protection of Critical Infrastructures against Explosives and CBRN

M.F. Pereira

Department of Condensed Matter Physics, Insitute of Physicss, CAS

Prague, Czech Republic

pereira@fzu.cz

CBRN and explosives typically have strong absorption signatures in the GHz, THz and Mid Infrared ranges of the spectrum (GIGA-TERA-MIR) and sometimes also in the NIR. Recent advances on theory and simulations of materials, sources, and detectors for this range [1-6] stimulate the search for new methods and solutions.

In order to develop further understanding for the development of new tunable GIGA-TERA-MIR sources, this paper summarises a hybrid Nonequilbrium Greens Functions (NEFG) and Boltzmann Equation approach for the optical and transport properties of semiconductor superlattice multipliers as sources of GHz-THz radiation. The results are successfully compared with experiments [1-2].  Figure 1 depicts a superlattice multiplier.

Fig1. Diagram of a semiconductor superlattice used a frequency multiplier.

In your ONE PAGE abstract, if possible, add a figure with a descriptive caption so that the referees can fully understand what it is about. Reference to papers should appear in the end.  I suggest to use some version of the first paragraph to make a connection between your research and the main goals of the Workshop. Please send your abstract to pereira@fzu.cz

References

[1] M.F. Pereira et al, Phys. Rev. B 96, 045306 (2017).

[2] M.F. Pereira et al, J. Nanophoton 11 (4), 046022 (2017).

[3] M.F. Pereira, Applied Physics Letters 109, 222102 (2016)

[4] C. I. Oriaku and M. F. Pereira, J. Opt. Soc. Am. B 34, 321-328 (2017).

[5] M. F. Pereira, Materials 11(1), 2 (2018);

[6] M.F. Pereira, Opt Quant Electron 47, 815–820 (2015).